## Slide 1: BED: A New Data Set for EEG-based Biometrics
By: Steven Cao

## Slide 2: Why biometric system?
Traditional access control approaches require individuals to remember or possess some information or item that must be presented to the access system.
  Problem
    Information can be forged or stolen
    Information can be hard to remember
Biometrics are an alternative to other more traditional access methods based on keys, ID cards, or passwords.
  Why?
    Instead of having to present info that can be forged to the access system, it requires the biological and behavioral characteristics of the individual.
  Examples
    Fingerprint recognition
    Face recognition
    Iris recognition
    Voice recognition

## Slide 3: Why EEG-based biometric system?
Electroencephalography (EEG) signals present some major advantages when compared to other biometrics modalities (ex. face, iris, voice)
  Resilient to physical injuries
  Extremely hard to reproduce
  Cannot be furtively captured at a distance

## Slide 4: Why consumer-grade devices for EEG-based biometrics?
Medical-grade devices
  Too expensive
  Tedious preparation needed for acquiring the signals
Consumer-grade devices
  Low-cost
  Simplify development in real-life scenarios
MUSE
Mind wave
CONSUMER-GRADE
MEDICAL-GRADE
Enobio
B-Alert
Brain Vision
Emotiv EPOC

## Slide 5: Previous Datasets Problems
The absence of a public standard benchmark that prevents a fair comparison between methods.
  Resulted in:
    People using public EEG datasets that were designed for a purpose other than EEG-based biometrics.
    Example
      University of California, Irvine (UCI): Concieved for alcoholism detection
      Visual evoked potentials (VEPs): Conceived for image speech
    People creating small private datasets
Little attention towards consumer-grade devices

## Slide 6: Why biometric EEG datasets should use different stimuli?
Biometric systems based on EEG signals should consider different stimuli in order to study their potential capabilities.
  Why?
    The person specific patterns contained in brain signals may strongly depend on many factors, including the task type the subject is performing.
  Types of Stimuli
    resting state (ex. eyes closed)
    cognitive tasks (ex. addition)
    sensory stimuli (ex. checkerboard)

## Slide 7: Why biometric EEG datasets should have multiple sessions?
Template aging (the increase in error rates caused by time-related changes in the biometric pattern).
  Problem
    Researchers use data acquired during a single session or have used several sessions but constructed the training and validation sets mixing the samples from all sessions, disregarding the acquisition date.
    This results in not examining the permanence of such patterns across time and thus their applicability for practical real-world EEG biometrics systems.
Data acquisition should happen over time, along several sessions.
  Why?
    To ensure the temporal stability (the stability of the content of reports across time) of the extracted patterns and the proposed solution.

## Slide 8: Data Set Design
BED: Biometric EEG Dataset
  Uses the Emotiv EPOC+ headset for EEG acquisition
  Includes EEG responses from 21 subjects
    18 boys
    3 girls
  Uses 12 different Stimuli
    Affective Stimuli
    Cognitive Stimuli
    Visual Evoked Potentials
    Resting State
  Contains data from 3 different chronologically disjointed sessions.
Emotiv EPOC wireless EEG headset
Notes: Talk about the different stimuli: key part of the BED dataset

## Slide 9: Affective Stimuli
Definition:
  A type of stimuli aimed to elicit typical emotional responses
Examples in this study
  Images selected to elicit specific emotions (ex. Spiders, bugs)
    Used the GAPED and OASIS data sets
Why we use Affective Stimuli?
  To facilitate future research on the influence of emotions on EEG-based biometric tasks

## Slide 10: Cognitive Stimuli
Definition
  A type of stimuli that involves conscious intellectual activity
Example in this study
  Mathematical Computation (two-digit additions)
Why do we use cognitive stimuli?
  Generate cognitive imagery-related patterns in the participant
  Bring the participant back to a neutral emotion state after been exposed to an affective stimulus.
  Check the participants engagement with the experimental process by checking the correctness of their answers.

## Slide 11: Visual Evoked Potentials
Definition
  The electrical potentials due to a brief visual stimuli which can be recorded from the scalp overlying visual cortex.
Examples in this study
  Visual Evoked Potentials at 2, 5, 7, 10 Hz - Standard checker-board pattern with pattern reversal
  Visual Evoked Potentials at 2, 5, 7, 10 Hz - Flashing with a plain color, set as black
Why do we use visual evoked potentials?
  Various researchers have proposed the use of VEP for the extraction of user-specific patterns from EEG signals.
Visual Evoked Potentials through checkerboards

## Slide 12: Resting State Stimuli
Definition
  The absence of any stimuli or task
Examples in this study
  Resting state with eyes closed
  Resting state with eyes open
Why do we use Resting State Stimuli?
  It has been largely adopted due to its simplicity

## Slide 13: Signal Acquisition
Device used for EEG acquisition
  The Emotiv EPOC+ system
    Low-cost EEG capturing device
    Equipped with 16 contact sensors, fixed on flexible plastic arms that are placed against the scalp of the user.
      Fourteen of the contacts
        AF3, F7, F3, FC5, T7, P7, O1, O2, P8, T8, FC6, F4, F8, and AF4 locations of the modified combinatorial nomenclature (MCN)
      Two contact sensors
        M1 and M2 mastoid locations for reference.
Sampling frequency
  14-channel EEG signals were captured at a sampling frequency of 256 Hz using the Emotiv EPOC+ [60] wireless EEG headset.
Environment setting
  Controlled illumination
  Isolated from sources of noise or distraction.
Emotiv EPOC wireless EEG headset

## Slide 14: Acquisition Protocol
Notes: I will not talk much about the acquisition protocol in these slides. If you want to see the full outline of the protocol, then read the paper

## Slide 15: Self-Assessment Manikin (SAM)
Definition
  The Self-Assessment Manikin (SAM) is a non-verbal pictorial assessment technique that directly measures the pleasure, arousal, and dominance associated with a person's affective reaction to a wide variety of stimuli.
What are we measuring?
  Valence: describes the extent to which an emotion is positive or negative
  Arousal: describes the intensity of the associated emotional state.

## Slide 16: Analysis of the Participant’s responses to the SAM
Results (correlation with the expected answer per subject
  The valence dimension shows pretty high average correlation scores of ρ = {0.8231, 0.8506, 0.8507} for the first, second, and third session, respectively.
  The arousal dimension presents significantly lower average correlation scores (ρ = {0.3701, 0.4183, 0.3299}).
Conclusions
  These figures show that the arousal scale is far more subjective than the valence one, and ratings may have a stronger dependency on the subjects’ background, thus showing a higher variance.

## Slide 17: Analysis of the Agreement Between Sessions
Results
  For valence, a median Kendall’s W = 0.9285 (p-value << 0.05) was obtained across participants
  For arousal, a median Kendall’s W = 0.7918 (p-value < 0.05 in all but five subjects).
Conclusions
  These values show a very high intersession agreement for valence ratings and a moderate one for arousal ratings.

## Slide 18: Baseline Results for Subject Verification Using the BED dataset
Evaluation process
  Data acquired during one session for enrolment, and data acquired at another later session to test the verification performance.
Evaluation process for the performance degradation due to time aging
  Trained the subject models with data from the first session and independently tested them by using data from the second and third sessions.
Patterns
  The average performance along all different types of stimuli decreases consistently with time
  The stimuli, affective image stimuli (AS) and resting state with the eyes closed (RC) seem to perform slightly better compared to other stimuli for verification performance.
Tables II and III show the subject verification results for each stimulus (columns) and EEG feature (rows).

## Slide 19: Baseline Results for Subject Identification Using the BED dataset
Method
  Data from sessions 1 and 2 were used for training and data from session 3 were used to test the trained models.
Conclusions
  MFCC features provide the best performance for the majority of stimuli. This is true for all cases except MC, RO, and VF7, for which the SPEC features provided the highest accuracy.
  The highest identification accuracy for each type of feature (MFCC, ARRC, and SPEC) was always achieved for the resting state with eyes closed (RC) stimulus